## Slide 1: Electronics Lab (Experiment-2)
P . Manoj Kumar
Roll no : 21IE10027

## Slide 2: Design and simulation of common emitter amplifier with stable operating point
Objective of the Experiment
Know how to stabilize operating point of a CE amplifier
Constructing an amplifier topology and bias the transistor in appropriate operating point for proper analog operation.
Observe and analyze “small signal” frequency response of the amplifier
Know the practical values of gain and band width of a simple voltage amplifier

## Slide 3: Part A: Compare bias point stability of CE amplifier with Fixed-bias and that with Self-bias
Procedure
The resistors of the common emitter amplifier with fixed-bias configuration (circuit-diagram-1)were chosen in such a way that the Vce is around 6V and Ic in 1- 2mA current range.
The transistor was replaced with another one having significantly different 𝛽F .
The change in DC operating point of the circuit was observed and analyzed.
The experiment steps 1-3 were repeated for a common emitter amplifier with self-bias configuration (circuit-diagram-2).

## Slide 4: Circuit Diagram-1
Fig-1.1-Circuit with unknown resistors with BJT (2N2222) in fixed-bias configuration

## Slide 5: Values of Biasing Resistances
The value of Rc wil be nearly =
Rb (in ) | Vce( in volt)
500 | 0.128733
700 | 0.176792
1000 | 2.8165
1400 | 5.26318
1500 | 5.68369
1585 | 6.00187
 | Vce( in volt)
500 | 0.128733
700 | 0.176792
1000 | 2.8165
1400 | 5.26318
1500 | 5.68369
1585 | 6.00187

## Slide 6: DC Operating Point Analysis
Fig-1.2-Operating point analysis of the circuit with BJT (2N2222) in fixed-bias configuration
Vce = 6.00187V and Ic = 1.49953mA

## Slide 7: DC Operating Point Analysis
Fig-1.3-Operating point analysis of the circuit with BJT (2N3904) in fixed-bias configuration
Vce = 3.25174V and Ic = 2.18706mA

## Slide 8: Change in Operating point Analysis
There is a significant change in the DC operating point after the changing the BJT(2N2222) to BJT(2N3904).
Operating Point Parameters | Circuit with BJT (2N2222) | Circuit with BJT (2N3904)
𝛽 | 200 | 300
Vce (in V) | 6.00187 | 3.25174
Ic (in mA) | 1.499 | 2.187

## Slide 9: Changing Values of Resistances
The value of Rc wil be nearly =
Rb (in ) | Vce( in volt)
1000 | 0.164937
1500 | 2.8007
2000 | 4.94092
2100 | 5.25465
2300 | 5.8052
2380 | 6.00102
 | Vce( in volt)
1000 | 0.164937
1500 | 2.8007
2000 | 4.94092
2100 | 5.25465
2300 | 5.8052
2380 | 6.00102

## Slide 10: DC Operating Point Analysis
Fig-1.4-Operating point analysis of the circuit with BJT (2N3904) in fixed-bias configuration after changing the values of resistances

## Slide 11: Circuit Diagram-2
Fig-1.5-Circuit in Self-Bias Configuration with unknown resistors with BJT (2N2222)

## Slide 12: Values of Biasing Resistances
Generally, VB =
= R1 = 2R2
Current through R1 and R2 is same ( ≈ 100Ib )
IC = 1.5 mA IB = mA
IR1 = IR2 = mA
= mA R1 + R2 = K𝛺
From Above two relations ,
R1 = K𝛺 , R2 = K𝛺

## Slide 13: Values of Biasing Resistances
As VBE is around 0.7V,
VE = 4V - 0.7V = 3.3 V
VC = VCE + VE = 9.3V
And the emitter current is ,
IE = Ic = 1.5 mA
The value of RC = =
The Value of RE = = 2.2
2N2222 : R1 = 10.67K𝛺 , R2 = 5.33K𝛺 , RC , RE = 2.19
2N3904 : R1 = 16K𝛺 , R2 = 8K𝛺 , RC , RE = 2.193

## Slide 14: DC Operating Point Analysis
Fig-1.6-Operating point analysis of the circuit in self-bias configuration with BJT (2N2222)
Vce = 5.98746V and Ic = 1.5029mA

## Slide 15: DC Operating Point Analysis
Fig-1.7-Operating point analysis of the circuit in self-bias configuration with BJT (2N3904)
Vce = 5.96773V and Ic = 1.50922mA

## Slide 16: Change in Operating point Analysis
There is no significant change in the DC operating point after the changing the BJT(2N2222) to BJT(2N3904). Both Vce and Ic are almost same.
Operating Point Parameters | Circuit with BJT (2N2222) | Circuit with BJT (2N3904)
𝛽 | 200 | 300
Vce (in V) | 5.99 | 5.96
Ic (in mA) | 1.503 | 1.509

## Slide 17: DC Operating Point Analysis
Fig-1.8-Operating point analysis of the circuit with BJT (2N3904) after changing the values of resistances in self-bias Configuration
Vce = 5.982V and Ic = 1.504mA

## Slide 18: Part B: Design and simulation of a CE amplifier with Self-bias
Procedure
Choose the components of the CE amplifier with self-bias configuration for Vce around 5V and Ic in 1-2mA (shown in Fig 2.c).
Observe the gain and phase response of the amplifier over a wide range of frequency [say, 20Hz to 1MHz].
Analyze the observed frequency response and compare it with theoretical calculation (based on values of transistor parameters and that of components).

## Slide 19: Circuit Diagram
Fig-1.9-Circuit in Self-Bias Configuration with unknown resistors with BJT (2N2222) and coupling capacitors

## Slide 20: Values of Biasing Resistances
From previous calculations,
R1 = 10.67 K𝛺 , R2 = 5.33 K𝛺
As VBE is around 0.7V,
VE = 4V - 0.7V = 3.3 V VC = VCE + VE = 8.3V
And the emitter current is ,
IE = Ic = 1.5 mA
The value of RC = =
The Value of RE = = 2.2 = 2.189K

## Slide 21: DC Operating Point Analysis
Fig-1.10-Operating point analysis of the circuit in Self-Bias Configuration with unknown resistors with BJT (2N2222)
and coupling capacitances Vce = 5.00019V and Ic = 1.5mA

## Slide 22: Gain and Phase Response of the Amplifier
Fig-1.11- Small signal AC analysis of the common emitter amplifier

## Slide 23: Observed Pole Frequencies
Fig-1.12-Circuit Diagram for calculation of poles
max_gain: MAX(mag(v(vout)))=(42.6434dB,0°) FROM 10 TO 1e+012
f1: mag(v(vout))=max_gain/sqrt(2) AT 1781.33 (First Pole Frequency)
f2: mag(v(vout))=max_gain/sqrt(2) AT 9.83598e+006 (Second Pole Frequency)

## Slide 24: Calculation of Pole Frequencies
First Pole Frequency (fL)
The first pole frequency is mainly due to the coupling and by-pass capacitances.
f1 = (Pole due to capacitance C1)
f2 = (Pole due to capacitance CX)
f3 = (Pole due to capacitance C2)
fL = max(f1,f2,f3) = 1853.417 Hz (which is close to 1781.33Hz)

## Slide 25: Calculation of Pole Frequencies
Second Pole Frequency (fH)
The second pole frequency is mainly due to the parasitic capacitances.
fH1 = = 79.808KHz
fH2 = = 8.3MHz

## Slide 26: Observations
Self-bias configuration of common emitter amplifier is the most stable configuration, as change in beta of the transistor doesn’t effect the operating point much, keeping the amplifier in a stable operating point.
The by-pass capacitor is generally used to increase the gain at high frequencies making the RE short.

## Slide 27: Thank You !